## Slide 1: Final Project Report “Wireless embedded system for human activities recognition using ESP32 and Jetson Nano”
Group 03 – NT131.O12.MMCL
Instructor: Assoc Prof. Lê Trung Quân

## Slide 2: Members of group 03 Tống Võ Anh Thuận Trần Công Hải
21522652
21520811

## Slide 3: 01 02 Project overview System architecture 03 04 System realization System demonstration Table of content

## Slide 4: Project overview 01
Introduction of the topic and related definitions

## Slide 5: In this project, we:
- Capture CSI signal data from Wi-Fi communication between embedded devices.
- Train a deep learning model to recognize human activities based on the CSI data.
- Publish prediction to an MQTT server for monitoring.

## Slide 6: About CSI signal
Channel State Information is a signal metric captured in communication systems
It allows data-symbols to be encoded in multiple subcarrier frequency
The CSI value for each subcarrier is defined as a complex number with a real component and an imaginary component

## Slide 7: About deep learning model
CSI data is complex => Use CNN model for this task
A Convolutional Neural Network (CNN) is a type of neural network that is well-known for tasks like image classification.
After researching, we find that it can be used to learn CSI signal data as well

## Slide 8: About MQTT protocol
MQ Telemetry Transport, is a lightweight messaging protocol designed for resource-constrained devices and low-bandwidth environments.
Operate in a pub-sub model.
=> Well-suited for the Internet of Things (IoT) communication

## Slide 9: System architecture 02
Key components of the system

## Slide 10: System architecture
TX
RX
Transmit CSI data via Wi-Fi
Send CSI data via serial port
ESP32 Microcontroller
Jetson Nano

## Slide 11: System architecture
TX
RX
*Performs activity*
(Process data and make prediction with CNN model)
Publish prediction
MQTT Broker
MQTT Client
Subscribe and receive prediction
Sampling rate: 100Hz ~ 100 pkt/s
Baud rate: 921600
<- 3 meters apart ->

## Slide 12: System realization 03
Configuration steps and training the model

## Slide 13: Configuration
Station mode
AP mode
ESP32 CSI Toolkit
+
ESP32 CSI Toolkit (stevenmhernandez.github.io)

## Slide 14: Training model
Data collection
Segmentation
Extract amplitude
Null filter
---->

## Slide 15: Training model
Dataset: 525 segments of 200 packets = 105,000 packets
Validation loss: 0.2469
Validation accuracy: 0.9324

## Slide 16: Model deployment

## Slide 17: Model deployment
.h5 format
.onnx format
.engine format
(optimized for inference efficiency)

## Slide 18: Set up MQTT Broker

## Slide 19: Build client application

## Slide 20: DEMO